## Slide 1
Using Visual Studio and VS Code for Embedded C/C++ Development
Marc Goodner, Principal Program Manager, Microsoft

## Slide 2: Mission of C++ Product Team at Microsoft (DevDiv)
Make the lives of all C++ developers on the planet better
  by participating with the C++ Standards committee
  by investing in the Microsoft Visual C++ (MSVC) Compiler
  by improving the Visual Studio IDE
  by continuing to enhance the C++ extension for Visual Studio Code

## Slide 3: Agenda
VS Code and mbed
Visual Studio and mbed
Visual Studio and Yocto SDKs
Visual Studio C++ Extensibility

## Slide 4: C/C++ extension for VS Code
Enables C/C++ IntelliSense, code browsing, code formatting, and debugging.
Over 6 million downloads since first shipped in Mach 2016.

## Slide 5: Demo: VS Code with mbed

## Slide 6: Linux C++ with Visual Studio

## Slide 7: Linux support for C++ in Visual Studio
Use Visual Studio with any Linux distro or Windows Subsystem for Linux (WSL)
  Remote system needs SSH, GDB, and GCC for compile
  Connect using user/password or private key
  IntelliSense supports GCC with standard Linux libraries
  Debug from your projects or attach to remote process
    Use either gdb or gdbserver on the remote
    Python pretty printer type visualizers supported in gdb mode
  Support for CMake 3.8+ (or MSBuild if you prefer)
https://aka.ms/vslinux

## Slide 8: Open Folder
Ideal for non-MSBuild projects
  e.g. CMake, make or other C++ build systems
Easy to get started
  devenv.exe <directory> or “File > Open > Folder…” (Ctrl+Alt+Shift+O)
Enables familiar VS experiences for any projects
  All C++ IntelliSense & code navigation operations
  External build system integration
  C++ debugging

## Slide 9: Internet of Things
Edit, build and debug in Visual Studio for IoT devices running Linux (E.g. Raspberry Pi, Beaglebone, Yocto SDKs with some configuration)
ARM GCC support
  Local cross compile uses ARM GCC compiler
  mbed folder-based project support
  Launch templates provided to illustrate how to debug devices
  http://aka.ms/vsgccarm
Notes: 4:03:15 - 4:04
0:48:15 - 0:49:00

## Slide 10: Demo: Visual Studio and mbed

## Slide 11: Visual Studio and Yocto SDKs
For Linux Visual Studio projects
  Create a solution with two Linux projects, one application and one makefile
  In the Application override x64 Project defaults to use Yocto cross compilers and sysroot on your build machine
  Post build event to copy output to the ARM configuration build output directory
  The ARM configuration connects to your device for debug but not build
  The makefile project should be configured to the same ARM device but is only used to copy the binary to the device
For CMake use the proper toolchain file for cross compile
  Use tasks to copy output to ARM device
  Configure launch targets to point to ARM device instead of build machine

## Slide 12: Demo: Visual Studio and Yocto
https://github.com/robotdad/LinuxCrossCompile

## Slide 13: Visual Studio C++ Extensibility
Application Types
  Provide ability to use the VC project and build system
  Props files that define static values
  Targets files embed MSBUILD Targets and Tasks
Toolsets within Application Types
  Allows the reuse of an application type platform with minimal rework
  Amount of extensibility depends on what Application Type provided
Property Pages
  XML files that define the Project Property Pages

## Slide 14: Start from an existing application type/toolset
Linux application type
  [VS install dir]\Common7\IDE\VC\VCTargets\Application Type\Linux
Linux remote GCC toolset
  1.0\Platforms\[arch]\PlatformToolsets\Remote_GCC_1_0
Create your own toolset in place, restart Visual Studio to use

## Slide 15: Visual Studio and VS Code extensions
Add-ons that can customize the Visual Studio experience
  Add your own items to menus and toolbars
  Extend existing tool windows or create your own
  Customize IntelliSense for a language or add support for a new one
  Create new project templates
The Visual Studio Marketplace provides a place to discover and publish extension to
  Over 700,000 extensions per month are downloaded from the marketplace

## Slide 16: Demo: Toolset in a VS Extension
https://github.com/robotdad/CrossCompileExtension

## Slide 17: Providing toolchains for CMake
Package your compiler and other tools in an extension
A CMake folder can be generated from a project template
  Include a CMake toolchain file for your compiler and a CMakeSettigns.json file that uses it
  Launch.vs.json to tailor launch settings for debug
  Tasks.vs.json showing how to run other tools that may be part of your solution

## Slide 18: Demo: CMake Toolchain
https://github.com/robotdad/CrossCompileExtension

## Slide 19: Visual Studio extension references
http://aka.ms/extendvs
GitHub samples repo:
https://github.com/Microsoft/
VSSDK-Extensibility-Samples

## Slide 20: VS Code extension resources
Docs:
https://code.visualstudio.com/docs/extensions/overview
Extension generator:
https://code.visualstudio.com/docs/extensions/yocode
Extension samples:
https://code.visualstudio.com/docs/extensions/samples

## Slide 21: Visual Studio C++ Linux Tips and Tricks
Verbose build output is very helpful for troubleshooting
Include files
  Mount /usr/include as a samba share
  Copy locally, e.g. scp -r root@192.168.2.15:/usr/include .
Unexpected debugging results we will ask for a log, from a Visual Studio command window in the IDE
  Debug.MIDebugLog /On:path-to-a-log-file
  Then try to debug your project. After the failure enter:
  Debug.MIDebugLog /Off
When using WSL check port 22 is available

## Slide 22: Linux C++ Resources
Feedback: “Report a problem” directly in the IDE
User Voice: https://visualstudio.uservoice.com/
Visual Studio C++ team:
Blog: https://blogs.msdn.microsoft.com/vcblog
Twitter: @visualc
Linux documentation: http://aka.ms/vslinux
Arm cross compile: http://aka.ms/vsarmgcc
Linux issues, discussion: https://github.com/microsoft/vslinux
Contact: vcpplinux-support@microsoft.com
Marc Goodner
mgoodner@microsoft.com
@robotdad